## Slide 1: CCAFS Case: Cassava processing
Industrialisation: effects on food loss, GHG emissions and local economy
2019, Bert Dijkink, Jan Broeze
Wageningen Food & Biobased Research
This work is implemented as part of the Consultative Group on International Agricultural Research (CGIAR) Research Program on Climate Change, Agriculture and Food Security (CCAFS), which is carried out with support from CGIAR Fund Donors and through bilateral funding agreements.

## Slide 2: Cassava processing: Introduction CCAFS
The Cassava processing in Mozambique is studied as one of the 4 cases in this CAFFS project.
The goal of the CCAFS project is to evaluate different interventions in the food chain on the effect on food security and Green House Gas (GHG) emissions.
Other cases:
  Milk chain: Evaluating different cold chain opportunities in Ethiopia.
  Hermetic Bags for the storage of Maize: analyse effectiveness for post harvest and quality losses; based on these outcomes the economical relevancy in perspective for farmers in different Sub-Sahara-Africa countries is assessed.
  Tomatoes: Reduction of post harvest losses by changes in transport.

## Slide 3: Cassava processing: introduction
Cassava is a security food for many people in Africa.
The Cassava roots are very perishable and the process it into a food ingredient is very labour intensive.
In this case three different types of industrialisations are compared on the GHG emission to recover the starch from the Cassava using in the brewery industry.

## Slide 4: Cassava processing: characteristics
Farmhouse processing
Dadtco mobile factory
Village processing
Central Factory

## Slide 5: Cassava processing: characteristics
Farmhouse processing
  Low productivity
  High losses (process)
  No investment
Dadtco mobile factory
  High productivity
  Low losses
  High investment
Village processing
  Better productivity
  High losses (process)
  Low investment
Central Factory
  High productivity
  High losses (raw material)
  High investment

## Slide 6: Cassava processing: yields
Losses by processing and estimated raw material rejection for the different processing ways

## Slide 7: Cassava processing: GHG Emissions
GHG emission of Cassava starch used in a brewery produced at different scales of industrialization, and compared with maize.
-31%
18%
25%
42% 39%

## Slide 8: Cassava processing: GHG emission
Processing Cassava to a starch cake in the mobile factory is an attractive option for both food security (minimal losses) and GHG emissions
  When processing to starch flour, energy use for drying results in higher GHG emissions
For the scenario of processing in the centralized factory both the emissions due to collection transport and due to losses are significant higher than the mobile factory scenarios
Due to the higher impact of agricultural production of imported Maize, the ‘Maize’ scenario has higher impacts than the cassava decentralized processing scenarios

## Slide 9: Cassava processing: Economics
Since the factory returns (annually) to the same locations, it becomes relevant to give training.
To secure the root supply, farmers are trained to increase their individual supply from 1,5 to 6,5 MT in three years.
One mobile plant with 5MT/h raw material capacity key figures
  Estimated yearly capacity (80MT/day * 300 days/y) 24000MT Roots, 6000MT/y Cassava flour
  Local economy: 200 jobs (203k€/y) + 816k€/y for the raw material
  Turnover: 6000MT Cassava Flour represent a benchmark value of 3M€ DDP (“Delivered Duty Paid”)
  Added value: 2,2M€/year

## Slide 10: Cassava processing: Conclusions
Processing Cassava to starch cake for use in the brewery in the mobile factory saves more than 50% of GHG emissions compared to a central Cassava factory.
Compared with commonly used starch source (Maize) a 25% GHG emissions is achieved.
The mobile factory show that small industrialization can have a significant regional economical grow with relative low impact of GHG emissions.
Financial health of the mobile plant still has to be proven in the field
  Depends mainly on the sales power